### Tech./Data Sheet

GREASE-A-WAY

| PRODUCT NAME GREASE-A-WAY MANUFACTURER & DISTRIBUTOR OF INDUSTRIAL CHEMICALS 8509 SUNSTATE ST. TAMPA, FLORIDA 33634 (813) 886-8811 PRODUCT DESCRIPTION GREASE-A-WAY is a ready-to-use degreaser for concrete, stone, and masonry surfaces. It is a water base cleaner with a co-solvent and surfactants to actively dissolve dirt and grease. BENEFITS GREASE-A-WAY provides safe and economical means for cleaning up stains and wax from concrete, stone, and masonry surfaces. It is easy to use and can be adjusted in strength to provide the cleansing power needed for a variety of soils. RECOMMENDED USES GREASE-A-WAY is recommended for surface preparation when applying SPRAY-DECK, TEXTURE-CRETE, THIN-CRETE, and NEW-CRETE. It also can be used as a general purpose cleaner of concrete, overlay systems, terrazzo, marble, quarry tile, and stone floors. | APPLICATION PROCESS For maintenance cleaning, add 20 parts water to 1 part GREASE-A-WAY. Spray or wipe on, being sure to cover entire area. Rinse with water and dry. For concrete surface preparation, use 4-8 fluid oz of GREASE-A-WAY degreaser to one gallon of water. Apply with a sprayer and agitate with a stiff broom. Allow to stand for 10 minutes and flush with water. For tough stains, apply GREASE-A-WAY uncut, and allow to stand for one hour. Flush with water and repeat if necessary. PACKAGING 1 gallon, 5 gallon pail, 55 gallon drum AVAILABILITY Available through distributors or contact manufacturer. TECHNICAL INFORMATION Refer to material safety data sheet. SAFETY PRECAUTIONS Irritant to eyes and skin, Do not swallow. If eye or skin contact is made, flush with water for 15 minutes. If swallowed, dilute with water. Wear rubber gloves and splash proof goggles. | WARRANTY All recommendations, statements and technical data contained herein based on tests we believe to be reliable and correct, but accuracy and completeness of said tests are not guaranteed and are not to be construed as a warranty, either expresses or implied. User shall rely on his own information and tests to determine suitability of the product for the intended use and user assumes all risk and liability resulting from his use of the product of this manufacturer which proves to be defective. Neither seller nor manufacturer shall be liable to the buyer or any third person having any injury, loss or damage directly or indirectly resulting from use of or inability to use the product. Recommendations or statements other than those contained in written agreement signed by an officer of the manufacturer shall not be binding upon the manufacturer or seller. |
| --- | --- | --- |