Material Safety Data Sheet

Increte Systems, Inc.

P. O. Box 151103

Tampa, Florida 33684

(813)886-8811   FAX (813)886-0188

Emergency Only 1-800-424-9300 (CHEMTREC)

International        1-202-483-7616

Issue Date:  October 1, 1996   Rev.Date June 27,2000

Page 1 of 2

Section I – Identification

HMIS Rating

Health:  2

Flammability  0

Reactivity:  1

Product Name:  Grease Away

Classification:  Cleaning product, aqueous solution

D.O.T. Hazard Class:  8, Corrosive Liquid, Basic, Inorganic, N.O.S.

(Contains Sodium Hydroxide, Sodium 					     Trioxosilicate)

UN3266, PG III

Section II – Components

Ingredient	C.A.S.#	Wt.%	PEL	  TLV	STEL	          Notes

Sodium gluconate	527-07-1	<3%

Sodium metasilicate	6834-92-0	<3%	2 mg/m3	    2 mg/m3		         Note 2.

Sodium hydroxide	1310-73-2	<3%	2 mg/m3	   2 mg/m3		         Notes 1,2.

Ethylene glycol Mono

Butyl ether	  111-76-2	<3%

Water and/or other non-		balance

hazardous or proprietary

Note 1:  Toxicity LD50 (IPR-mouse) (mg/kg) = 40.

Note 2:  Material is subject to SARA Title III, Section 312.

Section III – Physical Properties

Boiling Point:  >212oF (100oC)	Vapor Pressure:  n.a.

Melting Point:   n.a.	Vapor Density:  n.a.

Evaporation Rate:  n.a.	Specific Gravity:  ~1.10

Water Solubility:  Complete	Non-volatile:  6.5%

Physical Appearance:  Milky liquid.			pH:  10-12.

Section IV – Fire and Explosion Hazard Data

Flash Point:  n.a.	Explosion Limits (LEL):  n.a.			UEL:  n.a.

Extinguishing Media:  Use appropriate material for surrounding materials.

Hazardous Decomposition Products:  None.

Firefighting Procedures:  No special procedures required for this product.

Special Fire & Explosion Hazards:  Reacts with most metals to produce hydrogen gas, which can cause an explosive mixture with air.

Section V – Health Hazard Information

Primary Route(s) of Entry:  Eyes, skin, ingestion, and respiratory system.

Effects of Acute Overexposure:

Eyes – Will cause burning, stinging, tearing, and redness.  Can cause severe irritation and damage to eyes with possible blindness if not treated immediately.

Skin – Exposure can cause irritation, redness, and burning.

Respiratory – Overexposure can cause irritation of respiratory organs.  Prolonged or repeated exposure may cause pulmonary edema or lung inflammation.

Ingestion – Burning of mouth and throat, nausea and gastro-intestinal irritation.

First Aid:

Eyes – Flush gently with water for at least 15 minutes.  If symptoms persist or vision is impaired, seek medical attention.

Skin – Flush with water.  Wash affected areas with soap and water.  Seek medical attention if irritation persists.

Respiratory – Remove individual to fresh air.

Ingestion – DO NOT INDUCE VOMITING.  Drink large quantities of water followed by diluted vinegar or fruit juice.  Seek immediate medical attention.

Section VI – Chemical Reactivity

Stability:  Material is stable at normal temperatures.

Hazardous Polymerization:  Will not occur.

Incompatibility:  Strong acids, organic materials, most common metals, zinc, aluminum, magnesium, halogenated hydrocarbons.

Conditions to Avoid:  Contact with metals.

Hazardous Decomposition Products:  None known.

Section VII – Spill Procedures

Small Spill:  Neutralize with dilute hydrochloric acid and flush affected area with water.

Large Spill:  Wear full protective gear.  Stop leak at source, if possible.  Ventilate area.  Carfully neutralize spill with dilute acid and flush area with large amounts of water.  Use caution.

Waste Disposal Method:  Dispose of material in a manner consistent with local, state and federal regulations.

Section VIII – Special Protection Information

Respiratory Protection:  None required with normal usage.

Ventilation:  Mechanical ventilation not usually required, excepting indoor application with limited air exchange.

Gloves:  Neoprene or rubberized gloves.

Eye Protection:  Safety glasses.

Other Protective Equipment:  Wear appropriate work clothing to prevent skin contact.  Wash before reuse.

Section IX – Special Precautions

Handling and Storing:  Store separately.  Keep container tightly closed.  Avoid contamination with other chemicals.

Section X – Supplemental Information

The following materials are listed in SARA Title III, Section 312:

Sodium Hydroxide (1310-73-2)		CERCLA Reportable Quantity = 1000 lb

Sodium Metasilicate (6834-92-0)

This information is provided in good faith and is correct to the best knowledge of Inco Chemical Company, Inc.  Inco Chemical Co., Inc. makes no representation as to its completeness or accuracy. Customers are encouraged to make their own determination as to the suitability of this product for their purpose prior to use. Inco Chemical Co., Inc. disclaims responsibility for damages of any kind resulting from the use of this information.  No warranty of merchantability, fitness for use, or any other warranty is expressed or is to be implied regarding the accuracy of these data.